Raspberry Pi RaspberryPi 7-inch digital LCD screen for car

(1024*600 physical resolution with touch) == resistive screen

Computer Monitor HDMI

7.0-inch Digital LCD High Definition 1CH HDMI Interface

Product Features

○ Operating voltage: 5V power supply current requirements of 1A above 2A or less, such as the use of car power need to add a 5V regulator

○ Rated power: 6-7W

○ Signal Input: 1 channel HDMI

○ System system: PAL/NTSC

○ HDMI input: version HDMI 1.2

○Support 5V DC voltage input, you can also use USB, or mobile power supply, but you need to positive and negative poles can not be reversed, so as not to damage the circuit board.

○Resolution: 800 * 480 physical resolution, support the resolution range can be 640 × 480 --- 1600 × 1200 arbitrarily adjusted between!

○ Plug and Play function: support

○ OSD language: Simplified Chinese, Traditional Chinese, English, Japanese, Korean, Spanish, French, German, Italian, Portuguese

○ Control: Multi-function OSD operation or potential adjustment of brightness and color

○ Performance features: the use of mature programs, clear display effect

○ Support for image up/down/right/left/right flip, image 4:3/16:9 display format conversion

○ Scope of application: applied to visual intercom, car computer, instrumentation, industrial control, medical equipment, portable display devices and other electronic fields.

○ Working temperature: 0-60°C

Installation Dimension Drawing

Interface Function Description

| Bit number | Function | Remarks |
| --- | --- | --- |
| HDMI | HDMI Input | HDMI standard is 1.2 |
| J3 | Power input |  |
| J7 | LED Backlight Holder |  |
| CON1 | TTL-50PIN signal output |  |
| J6 | Pushbutton，Remote Control，LED Indicator Interface |  |
| J5 | Upgrade Program Interface | For factory upgrade |

Detailed description of interface functions

J6 Keypad, Remote Control Input Connector

| Serial number | Definition | Description |
| --- | --- | --- |
| 1 | 5V | Remote control power supply, actually 3.3V. |
| 2 | GND | GND |
| 3 | IR | Remote control input |
| 4 | POWER | Power on/off function |
| 5 | MENU | Menu display function |
| 6 | + | Add |
| 7 | _ | Minus |
| 8 | SOURCE | Signal source changeover |
| 9 | LED-R | LED Indicator |
| 10 | LED-G | LED Indicator |

J3-DCIN Power Interface

| Serial number | Definition | Description |
| --- | --- | --- |
| 1 | +5V | Positive power input |
| 2 | +5V | Positive power input |
| 3 | GND | GND |
| 4 | GND | GND |

HDMI Interface

| Serial number | Definition | Description |
| --- | --- | --- |
| 1 | HDMI standard interface | Standard cables available |

J5, Upgrade Interface

| Serial number | Definition | Description |
| --- | --- | --- |
| 1 | SCL | SCL Upgrade Ports |
| 2 | SDA | SDA Upgrade Ports |
| 3 | GND | GND |
| 4 | NC | NC |

CON1, Interface Definition