### 1、install libinput,

Check the ”/usr/share/X11/xorg.conf.d/”directory for ”40 - libinput. Conf”.

If not, you need to install it, and if there is, skip to part 3.

sudo apt-get install xserver-xorg-input-libinput

### 2、copy this file to /etc/X11/xorg.conf.d/

The directory xorg.conf.d may not be in /etc/x11 at first, so you need to create it yourself.

sudo mkdir xorg.conf.d

### 3、Go to /etc/x11/xorg.conf.d/ and modify the 40-libinput.conf file

cd/etc/X11/xorg.conf.d/

sudo vim 40-libinput.conf

Find touchscreensection

Section"InputClass"

Identifier "libinput touchscreencatchall"

MatchIsTouchscreen "on"

MatchDevicePath "/dev/input/event*"

Driver "libinput"

EndSection

add Option "CalibrationMatrix" "0 -1 1 1 0 0 0 0 1”

It was eventually modified to look like this

Section"InputClass"

Identifier "libinput touchscreencatchall"

Option "CalibrationMatrix" " 0 -1 1 1 0 0 0 0 1“

MatchIsTouchscreen "on"

MatchDevicePath "/dev/input/event*"

Driver "libinput"

EndSection

Complete the above steps to perform a 270degree rotation.

Finally reboot.

Note:

90 degree rotation:Option "CalibrationMatrix" "0 1 0 -1 0 1 0 0 1"

180 degree rotation:Option "CalibrationMatrix" "-1 0 1 0 -1 1 0 0 1"

270 degree rotation:Option "CalibrationMatrix" "0 -1 1 1 0 0 0 0 1"